## Slide 1: LAB 1 INTRODUCTION TO VHDL
EXERTED FROM DR. ADNAN SHAOUT- THE UNIVERSITY OF MICHIGAN-DEARBORN
FACULTY OF ENGINEERING
CAIRO UNIVERSITY
CMPN301: COMPUTER ARCHITECTURE COURSE

## Slide 2: DESIGN FLOW
HDL Design
Behavioral Simulation
Synthesis
Post-Synthesis Simulation
Floor Planning
Placement
Routing
DRC / LVS
Post- Route Simulation
Fabrication
Leonardo
Modelsim
Computer Architecture
IC Station
Calibre
Notes: Synthesis:
  Translating the HDL code into a circuit, which is then optimized
Register Transfer Level (RTL):
  Type of behavioral model used for instance for synthesis

## Slide 3: OBJECTIVES
Define VHDL and its usage
Understand different modeling techniques in designing digital circuits (Dataflow , structural)
Understand the Hardware created from the VHDL code
Understand Concurrent statement
Reuse previously created entity (component instantiation a.k.a port mapping)
Practice designing with VHDL

## Slide 4: WHAT IS VHDL?
VHSIC Hardware Description Language
VHDL is a programming language that allows one to model and develop complex digital systems.

## Slide 5: WHY VHDL?
Requirements specification
Documentation
Testing using simulation
Formal verification
Synthesis
Class assignments ☺

## Slide 6: HW DESIGNER GOAL
Most ‘reliable’ design process, with minimum cost and time.
Avoid design errors!

## Slide 7: VHDL is Describing Hardware so every line counts and cost a lot in real world

## Slide 8: VHDL LANGUAGE: VARIABLES
Variables are Wires
Assignment are “<=” or “:=” instead of “=”
  X <= C and D;
  W <= E nor F;
X
C
D
AND
E
F
NOR
W

## Slide 9: VHDL LANGUAGE: MODEL DEFINITION
Images are from http://vlsiuniverse.blogspot.com.eg/2016/07/multiplexer.html

## Slide 10: VHDL LANGUAGE: MODEL DEFINITION …(CONT)
Modules
Models
Entities
Components
System
ENTITY mux2 IS PORT ( IN1,IN2,SEl : IN std_logic; OUT1 : OUT std_logic); END ENTITY mux2;
entity name
port names
port mode (direction)
reserved words
punctuation
port type

## Slide 11: VHDL LANGUAGE: MODEL IMPLEMENTATION
ARCHITECTURE arch1 OF mux2 IS
BEGIN
out1 <= (in1 and (not Sel))
or
(in2 and Sel);
END arch1;

## Slide 12: LET’S MAKE A MUX 4X1

## Slide 13: MUX 4X1
ENTITY mux4 IS
PORT( in0,in1,in2,in3: IN std_logic;
sel : IN std_logic_vector (1 DOWNTO 0);
out1: OUT std_logic);
END mux4;

## Slide 14: VHDL LANGUAGE: MODEL IMPLEMENTATION
MODEL Implementation is called Architecture
Types of Modeling:
  Dataflow
    Describes the flow of data within a component/system.
  Structural
    Describes the component by the interconnection of lower level components/primitives
  Behavioral (next time)
    Describes the functionality of a component/system usually using a process
  Mixed of the above ways
Notes: there is no clear distinction between behavioral model and Dataflow
check this link http://stackoverflow.com/questions/18682019/confusion-between-behavioural-and-dataflow-model-programs-in-vhdl
-- this part is for understanding how to think of the design

## Slide 15: VHDL LANGUAGE: MODEL IMPLEMENTATION DATA FLOW
ARCHITECTURE arch1 OF mux4 IS
BEGIN
out1 <= in0 WHEN sel(0) = ‘0’ AND sel(1) =‘0’
ELSE in1 WHEN sel(0) = ‘0’ AND sel(1) =‘1’
ELSE in2 WHEN sel(0) = ‘1’ AND sel(1) =‘0’ ELSE in3;
END arch1;

## Slide 16: VHDL LANGUAGE: MODEL IMPLEMENTATION STRUCTURAL
Can we Make Mux 4x1 from Mux 2x1 ?

## Slide 17: VHDL LANGUAGE: MODEL IMPLEMENTATION STRUCTURAL

## Slide 18: VHDL LANGUAGE: MODEL IMPLEMENTATION STRUCTURAL
ARCHITECTURE struct OF mux4 IS
COMPONENT mux2 IS PORT (IN1,IN2,SEl: IN std_logic; OUT1 : OUT std_logic); END COMPONENT ;
SIGNAL x1,x2 : std_logic;
Begin
Signal are considered as wires
Signal type Notice there is no direction for signals
When we use another entity inside our architecture we call it component

## Slide 19: VHDL LANGUAGE: MODEL IMPLEMENTATION STRUCTURAL
ARCHITECTURE struct OF mux4 IS
COMPONENT mux2 IS PORT (IN1,IN2,SEl: IN std_logic; OUT1 : OUT std_logic); END COMPONENT ;
SIGNAL x1,x2 : std_logic;
Begin
Signal are considered as wires
Signal type Notice there is no direction for signals
When we use another entity inside our architecture we call it component
Till here we told our circuit that there is a component called mux2 and this is how to connect to it but we didn’t use it yet

## Slide 20: VHDL LANGUAGE: MODEL IMPLEMENTATION STRUCTURAL (CONT)
BEGIN
u0: mux2 PORT MAP (in0,in1,s(0),x1);
u1: mux2 PORT MAP (in2,in3,s(0),x2);
u2: mux2 PORT MAP (x1,x2,s(1),out1);
END struct;
Label to identify component with while tracing
Component name
Keyword , whenever I port map a component
I put it in the circuit (as hardware IC)
Parameters sent to the component in the same order they are mentioned in the declaration
Concurrent statements
All executes at the same time

## Slide 21: VHDL LANGUAGE: MODEL IMPLEMENTATION STRUCTURAL (CONT)
BEGIN
u0: mux2 PORT MAP (in0,in1,s(0),x1);
u1: mux2 PORT MAP (in2,in3,s(0),x2);
u2: mux2 PORT MAP (x1,x2,s(1),out1);
END struct;

## Slide 22: VHDL LANGUAGE: MODEL IMPLEMENTATION STRUCTURAL (CONT)
ENTITY gate_logic IS
PORT( A,B,: IN std_logic;
C: OUT std_logic);
END gate_logic;

## Slide 23: VHDL LANGUAGE: MODEL IMPLEMENTATION STRUCTURAL (CONT)
ARCHITECTURE and_gate OF gate_logic IS
BEGIN
c <= a AND b;
END and_gate;
ARCHITECTURE or_gate OF gate_logic IS
BEGIN
c <= a OR b;
END or_gate;

## Slide 24: VHDL LANGUAGE: MODEL IMPLEMENTATION STRUCTURAL (CONT)
ENTITY gates IS
PORT( in0,in1,in2,in3: IN std_logic;
out1, out2: OUT std_logic);
END gates;

## Slide 25: VHDL LANGUAGE: MODEL IMPLEMENTATION STRUCTURAL (CONT)
ARCHITECTURE struct OF gates IS
COMPONENT gate_logic IS PORT (A,B: IN std_logic; C : OUT std_logic); END COMPONENT ;
Begin
Till here we told our circuit that there is a component called gate_logic and this is how to connect to it but we didn’t use it yet

## Slide 26: VHDL LANGUAGE: MODEL IMPLEMENTATION STRUCTURAL (CONT)
BEGIN
and1: work.gate_logic(and_gate) PORT MAP (in0,in1,out1);
or1: work.gate_logic(or_gate) PORT MAP (in2,in3,out2);
END struct;

## Slide 27: DATA TYPE (STD_LOGIC)
Include
  Library ieee;
  Use ieee.std_logic_1164.all
Std_logic Possible values
  1 or 0
  X → for conflict
  Z → high impedance (remember tristate buffer?)
  U → undefined
  others
Think: What do you think possible values of Data Type (bit) ?
Which is better to use bit or std_logic?

## Slide 28: DATA TYPE (STD_LOGIC_VECTOR)
Std_logic_vector
  a,b : in std_logic_vector(2 downto 0)
  Can be accessed like b(2) , b(1)
To access all vector
  a <= b;
To access a range of the vector
  b(1 downto 0) <= a(2 downto 1)
‘&’ operator to concatenate two vectors or vector and single element
  b(1 downto 0 ) <= a(2) & ‘0’

## Slide 29: Still confused !!
Consider the module as a function or class
The entity declaration is like a header for the function (interface to our module)
The architecture is the implementation of the function (how this module behaves inside)
Whenever I want to use function in another , I have to include that function header (that’s when I introduce the module between architecture and begin)
The actual usage of the function happens when we call it – function call- this is like port mapping a component But …

## Slide 30: Important Consideration
Whenever you use port map , you add a component to the circuit , it is not like a function that you can call it and re-call it. so in our previous example we had 3 mux2 components (i.e. 3 ICs on the breadboard).
Since port mapping is physical insertion of hardware it can’t be made in a condition (i.e. x< = mux2 port map(…) when A=‘0’ ; is totally incorrect)
Unlike software , VHDL statement are concurrent , they all execute in the same time not after each other (unless in certain cases to be mentioned later)

## Slide 31: OBJECTIVES
Define VHDL and its usage
Understand different modeling techniques in designing digital circuits (Dataflow , structural)
Understand the Hardware created from the VHDL code
Understand Concurrent statement
Reuse previously created entity (component instantiation a.k.a port mapping)
Practice designing with VHDL

## Slide 32: TIPS
Always Save & Compile before simulation.
Read the Error/Warning messages in “Transcript” tap.
Change the “Radix” to make the simulation easier (right click on signal name in simulation).
Re-writing your code all over again will NOT solve your problems.
For any Error, check the few lines before the line with error message.
Always use Do files instead of Changing the inputs every time.

## Slide 33: DEMO#1
Create Project
Add files to project (and.vhd)
Compile (Fix Errors)
Simulate (force, clock, do)

## Slide 34: SUMMARY
What is VHDL?
Why VHDL
Entity/Architecture
Modeling using (Dataflow , structural)
Data types in VHDL (std_logic / bit & std_logic_vector / bit_vector)
Code is Concurrent not sequential
Signals are wires
Resuing previously created entity (component instantiation a.k.a port mapping)