## Slide 1: LAB 2 INTRODUCTION TO VHDL
EXERTED FROM DR. ADNAN SHAOUT- THE UNIVERSITY OF MICHIGAN-DEARBORN
FACULTY OF ENGINEERING
CAIRO UNIVERSITY
CMPS301: COMPUTER ARCHITECTURE COURSE

## Slide 2: What we learned last time
How to create Entity
How to implement Architecture
What different modeling could be used (Dataflow , behavioral, structural)
Code is Concurrent not sequential
“WHEN … ELSE” statement is concurrent only
Signals are wires
Different data types
How to reuse previously created entity (component instantiation a.k.a port mapping)
Architecture course
Intro to VHDL
2

## Slide 3: Objectives
Review Conditional Concurrent statements
Others Keyword
Learn about Generic entities
Learn about For-Generate
Architecture course
Intro to VHDL
3

## Slide 4: Remember Mux4x1
ENTITY mux IS
PORT( in0,in1,in2,in3: IN std_logic;
sel : IN std_logic_vector (1 DOWNTO 0);
out1: OUT std_logic);
END mux4;
Architecture course
Intro to VHDL
4

## Slide 5: When … ELSE / With … Sel
Architecture course
Intro to VHDL
5
ARCHITECTURE a_mux OF mux
BEGIN
out1 <= in0 WHEN sel = “00”
ELSE in1 WHEN sel = “01”
ELSE in2 WHEN sel =“10” ELSE in3;
END a_mux;
ARCHITECTURE b_mux OF mux
BEGIN
with sel select
out1 <=
  in0 when "00",
  in1 when "01",
  in2 when "10",
  in3 when "11";
END b_mux;

## Slide 6: When … ELSE / With … Sel
Architecture course
Intro to VHDL
6

## Slide 7: When … ELSE / With … Sel
What happens if we missed a case ?!
Architecture course
Intro to VHDL
7
F <= a when Sel = “00”;
-- what is the Value of F if Sel is not 00 ?!!!!

## Slide 8: When … ELSE / With … Sel
What happens if we missed a case ?!
A latch will be formed to save previous value
Architecture course
Intro to VHDL
8
F <= a when Sel = “00”;
-- what is the Value of F if Sel is not 00 ?!!!!

## Slide 9: Objectives
Review Conditional Concurrent statements
Others Keyword
Learn about Generic entities
Learn about For-Generate and if-Generate
Architecture course
Intro to VHDL
9

## Slide 10: “OTHERS” Keyword
Use “OTHERS” Whenever you want to:
  Set a bus to several zeros or several 1s but you don’t want to write it.
Example set F to 32 zero
Architecture course
Intro to VHDL
10
F <= “00000000000000000000000000000000”;
F <= x“00000000”; -- hexdecimal
F<= (Others => ‘0’);

## Slide 11: “OTHERS” Keyword
Use “OTHERS” Whenever you want to:
  Set a bus to several zeros or several 1s but you don’t want to write it.
  Set a certain bit to value and others zero
Example
Architecture course
Intro to VHDL
11
F <= “00000000000000000000000010000000”;
F <= x“00000080”; -- hexdecimal
F<= (7=>‘1’, Others => ‘0’);

## Slide 12: “OTHERS” Keyword
Use “OTHERS” Whenever you want to:
  Set a bus to several zeros or several 1s but you don’t want to write it.
  Set a certain bit to value and others zero
  Generic Case in Switch Cases
Example
Architecture course
Intro to VHDL
12
With S select
F <= a when “0010”,
b when others;

## Slide 13: Objectives
Review Conditional Concurrent statements
Others Keyword
Learn about Generic entities
Learn about For-Generate and if-Generate
Architecture course
Intro to VHDL
13

## Slide 14: Let’s build a full adder ☺
Architecture course
Intro to VHDL
14

## Slide 15: 1bit-adder example
ENTITY my_adder IS -- single bit adder PORT( a,b,cin : IN std_logic; s,cout : OUT std_logic); END my_adder;
ARCHITECTURE a_my_adder OF my_adder IS
BEGIN s <= a XOR b XOR cin; cout <= (a AND b) or (cin AND (a XOR b));
END a_my_adder;
Architecture course
Intro to VHDL
15

## Slide 16: Now how to build 4-bits full adder from 1-bit full adder?
Architecture course
Intro to VHDL
16

## Slide 17: Carry-Propagate Adder
Architecture course
Intro to VHDL
17

## Slide 18: 4 Bit-full Adder
Architecture course
Intro to VHDL
18
ENTITY my_nadder IS
PORT (a, b : IN std_logic_vector(3 DOWNTO 0) ;
cin : IN std_logic;
s : OUT std_logic_vector(3 DOWNTO 0);
cout : OUT std_logic);
END my_nadder;

## Slide 19: 8 Bit-full Adder
ARCHITECTURE a_my_nadder OF my_nadder IS
COMPONENT my_adder IS
PORT( a,b,cin : IN std_logic; s,cout : OUT std_logic);
END COMPONENT;
SIGNAL temp : std_logic_vector(4 DOWNTO 0);
BEGIN
  Temp(0) <= cin;
  f0: my_adder PORT MAP(a(0),b(0),temp(0),s(0),temp(1));
  f1: my_adder PORT MAP(a(1),b(1),temp(1),s(1),temp(2));
  f2: my_adder PORT MAP(a(2),b(2), temp(2),s(2),temp(3));
  f3: my_adder PORT MAP(a(3),b(3), temp(3),s(3),temp(4));
  Cout <= temp(4);
END a_my_nadder;
Architecture course
Intro to VHDL
19

## Slide 20: From Specific to Generic entities
Architecture course
Intro to VHDL
20
ENTITY my_nadder IS
PORT (a, b : IN std_logic_vector(3 DOWNTO 0) ;
cin : IN std_logic;
s : OUT std_logic_vector(3 DOWNTO 0);
cout : OUT std_logic);
END my_nadder;
Now how can we change 4-bits full adder to generic n-bit full adder?

## Slide 21: From Specific to Generic entities
Architecture course
Intro to VHDL
21
ENTITY my_nadder IS
PORT (a, b : IN std_logic_vector(n-1 DOWNTO 0) ;
cin : IN std_logic;
s : OUT std_logic_vector(n-1 DOWNTO 0);
cout : OUT std_logic);
END my_nadder;
Notice the use of ‘n’ here
But where did we define “n”

## Slide 22: From Specific to Generic entities
Architecture course
Intro to VHDL
22
ENTITY my_nadder IS
GENERIC (n : integer := 8);
PORT (a, b : IN std_logic_vector(n-1 DOWNTO 0) ;
cin : IN std_logic;
s : OUT std_logic_vector(n-1 DOWNTO 0);
cout : OUT std_logic);
END my_nadder;
Notice the use of ‘n’ here
But where did we define “n”
Add generic input
8 is default value and could be override while instantiation
Integer another data type

## Slide 23: 8 Bit-full Adder
ARCHITECTURE a_my_nadder OF my_nadder IS
COMPONENT my_adder IS
PORT( a,b,cin : IN std_logic; s,cout : OUT std_logic);
END COMPONENT;
SIGNAL temp : std_logic_vector(4 DOWNTO 0);
BEGIN
temp(0) <= cin;
f0: my_adder PORT MAP(a(0),b(0),temp(0),s(0),temp(1));
f1: my_adder PORT MAP(a(1),b(1),temp(1),s(1),temp(2));
f2: my_adder PORT MAP(a(2),b(2), temp(2),s(2),temp(3));
f3: my_adder PORT MAP(a(3),b(3), temp(3),s(3),temp(4));
Cout <= temp(4);
END a_my_nadder;
Architecture course
Intro to VHDL
23

## Slide 24: 8 Bit-full Adder
ARCHITECTURE a_my_nadder OF my_nadder IS
COMPONENT my_adder IS
PORT( a,b,cin : IN std_logic; s,cout : OUT std_logic);
END COMPONENT;
SIGNAL temp : std_logic_vector(n DOWNTO 0);
BEGIN
temp(0) <= cin;
f0: my_adder PORT MAP(a(0),b(0),temp(0),s(0),temp(1));
f1: my_adder PORT MAP(a(1),b(1),temp(1),s(1),temp(2));
f2: my_adder PORT MAP(a(2),b(2), temp(2),s(2),temp(3));
f3: my_adder PORT MAP(a(3),b(3), temp(3),s(3),temp(4));
Cout <= temp(4);
END a_my_nadder;
Architecture course
Intro to VHDL
24
Change size of signal

## Slide 25: 8 Bit-full Adder
ARCHITECTURE a_my_nadder OF my_nadder IS
COMPONENT my_adder IS
PORT( a,b,cin : IN std_logic; s,cout : OUT std_logic);
END COMPONENT;
SIGNAL temp : std_logic_vector(n DOWNTO 0);
BEGIN
temp(0) <= cin;
loop1: FOR i IN 0 TO n-1 GENERATE
fx: my_adder PORT MAP(a(i),b(i),temp(i),s(i),temp(i+1));
END GENERATE;
Cout <= temp(n);
END a_my_nadder;
Architecture course
Intro to VHDL
25
Change size of signal
i →is not visible outside the for generate

## Slide 26: For….Generate
We use it when we want to generate more than one component of the same type
loop1: FOR i IN 0 TO n-1 GENERATE
fx: my_adder PORT MAP(a(i),b(i),temp(i-1),s(i),temp(i));
END GENERATE;
The (for …generate) is not a Software Sequential loop .. It is like writing this line n times and they execute concurrently. Generates N hardware
Architecture course
Intro to VHDL
26
i →is not visible outside the for generate
i →is not visible outside the for generate

## Slide 27: Generic ….cont.
So after I made my entity generic when I instantiate I do the following
u0: my_nadder GENERIC MAP (16) PORT MAP (……)
Architecture course
Intro to VHDL
27
I indicate here the value of the generic data
Generic could be more than one parameter like generic (n,m : integer;)
Even could be with different type

## Slide 28: Generic ….cont.
In simulation
vsim my_nadder –g<genericName>=<value>
Example
Architecture course
Intro to VHDL
28
vsim my_nadder –gn=8

## Slide 29: Common Errors
During Coding:
  Mix the use of bit & std_logic
  Using port map inside a condition
  Size of Input Vector not Equal Size of Output Vector
During Simulation:
  Simulating without compiling last changes
  Not forcing all input ports at initialization
  Force values on output port/signal
Architecture course
Intro to VHDL
29

## Slide 30: Summary
Review on (When .. Else / With…Sel)
Use of “OTHERS” keyword
Make Generic Entities & use them
Use “for … Generate”
Architecture course
Intro to VHDL
30